## Slide 1: OpenPET software GUI design schemes
Qiyu Peng

## Slide 5: Programming Tools / Environment
 | DB | DUC | MB | CUC | Host PC
FPGA Firmware | X | X | X | X | 
Embedded MCU Software (NIOS) |  | X | X | X | 
PC Software |  |  |  |  | X
X: VHDL (Altera Quartus II ver. 12.0)
X: C (Altera Nios II EDS ver. 12.0)
X: C (NI LabWindows CVI 2009)

## Slide 6: C programing style guidelines
Based on “C Style Guide” suggested by Software Engineering Laboratory (SEL), the National Aeronautics and Space Administration (NASA) in 1994.
Rules and guidelines are used to guarantee the readability and maintainability of the C source codes (details are in my word file)

## Slide 7
Host PC software
Modular Design
Simple and easy to use
Upgradable
Main Functions
System configuration and system diagnosis
Data acquisition
Data analysis

## Slide 8: Software Requirement Analysis
System configuration and test
(GUI and scripts)
System configuration database
System HW/FW
DAQ configuration and DAQ
(GUI and scripts)
System HW/FW
List mode data (with a head file)
Data analysis and visualization
(GUI and scripts)
List mode data (with a head file)
Data analysis reports
System calibration and characterization
(control console and scripts)

## Slide 9: Head file format
File name
Date and time
Data type
Data collection time
Software version
Firmware version
User defined comments

## Slide 10: Event words and status words
In general, there are two kinds of words in the OpenPET list mode data:
Event words, include
-- Single event words, and
-- Coincidence
Status words transmit information other than the event data to the host PC, such as:
-- Event data format
-- Time information
-- Single or coincidence event rate
-- System configuration and status
-- Application-specific information such as patient bed position, transmission source position, system temperature, ECG signal, gate signal and etc.

## Slide 11: Event words
Event word path
DUC
Generate original single event data
DB
Add 3-bit DB
address to the
single event data
MB
Add 3-bit DUC
address to the
single event data
CUC
Add 3-bit MB address to single event data.
Generate coincidence event data (optional).
Insert status words to the data stream.
Host PC
Generate original single event data
DB
CDUC
Add 3-bit DB address to single event data.
Generate coincidence event data (optional).
Insert status words to the data stream.
Host PC
DUC
Generate original single event data
DB
Add 3-bit DB
address to the
single event data
CUC
Add 3-bit DUC address to single event data.
Generate coincidence event data (optional).
Insert status words to the data stream.
Host PC

## Slide 12: Event data length
Data from DBDUC, DUC MB and MBCUC
Single event data only
32-bit mode or 64-bit mode.
Data from CUC  host PC
Single event data, coincidence event data and status words.
32-bit mode, 64-bit mode, and 128-bit mode.

## Slide 13: Data paths and data mode combinations
DB
DUC
MB
CUC
Host PC
32 bits
32 bits
32 bits
32 bits
DB
DUC
MB
CUC
Host PC
32 bits
32 bits
32 bits
64 bits
DB
DUC
MB
CUC
Host PC
64 bits
64 bits
64 bits
64 bits
DB
DUC
MB
CUC
Host PC
64 bits
64 bits
64 bits
128bits
16 system clocks
8 system clocks
Oscilloscope mode

## Slide 14: DBDUC, DUC MB and MBCUC
32-bit data (8 system clocks)
General definition
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0
MB address
DUC address
DB address
Block address
Crystal ID
Payload
1
Crystal ID

## Slide 15: DBDUC, DUC MB and MBCUC
32-bit mode (8 system clocks)
Payload definition
-- Time mode – Bit 10~0, TDC data bits (11 bits, LSB: 50ps).
-- Energy mode – Bit 10~0, energy data bits (11 bits).
-- Test mode1 – Bit 10~0, test pattern data: 10101010101.
-- Test mode2 – Bit 10~0, test pattern data: 01010101010.
-- Anger-logic flood map plot mode – Bit 18, not used,
Bit 17~9, Y value (9 bits), Bit 8~0, X value (9 bits).
-- User-defined mode 1 - 11 bits of payload
-- User-defined mode 2 - 14 bits of payload
-- User-defined mode 3 - 17 bits of payload
-- User-defined mode 4 - 22 bits of payload
-- User-defined mode 5 - 25 bits of payload
-- User-defined mode 6 - 28 bits of payload
Standard
User-defined

## Slide 16: DBDUC, DUC MB and MBCUC
32-bit mode (Oscilloscope mode)
General definition
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0
MB address
DUC address
DB address
Channel address
Raw ADC data
1
Data counter
Unused
The maximum length of the raw data train is 64

## Slide 17: DBDUC, DUC MB and MBCUC
64-bit data (16 system clocks)
General definition

## Slide 18: DBDUC, DUC MB and MBCUC
32-bit mode (8 system clocks)
Payload definition
-- Time mode – Bit 10~0, TDC data bits (11 bits, LSB: 50ps).
-- Energy mode – Bit 10~0, energy data bits (11 bits).
-- Test mode1 – Bit 10~0, test pattern data: 10101010101.
-- Test mode2 – Bit 10~0, test pattern data: 01010101010.
-- Anger-logic flood map plot mode – Bit 18, not used,
Bit 17~9, Y value (9 bits), Bit 8~0, X value (9 bits).
-- User-defined mode 1 - 11 bits of payload
-- User-defined mode 2 - 14 bits of payload
-- User-defined mode 3 - 17 bits of payload
-- User-defined mode 4 - 22 bits of payload
-- User-defined mode 5 - 25 bits of payload
-- User-defined mode 6 - 28 bits of payload
Standard
User-defined

## Slide 19: CUC  host PC
Single event mode
In single event data mode (including the 32-bit raw ADC data mode), the formats of the data from CUC/CDUC host PC are the exactly the same that those defined in previous section (DBDUC, DUC MB and MBCUC).

## Slide 20: CUC  host PC
Coincidence event mode
Two 32-bit single event data  one 64-bit coincidence event data
Two 64-bit single event data  one 128-bit coincidence event data
Two 32-bit single event data  one 32-bit coincidence event data
Two 64-bit single event data  one 64-bit coincidence event data
MB address
DUC address
DB address
Block address
Crystal ID
Payload
1
Crystal ID
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0
MB address
DUC address
DB address
Block address
Crystal ID
Payload
Valid
Crystal ID
Single Event 1
Single Event 2
47
46
45
44
43
42
41
40
39
38
37
36
35
34
33
32
63
62
61
60
59
58
57
56
55
54
53
52
51
50
49
48

## Slide 21: Status word (fixed to 64 bits)
General definition

## Slide 22: Decoding List Mode Binary Data

## Slide 23
Data In
Status word
Event word
Single Event
Coincidence event
Raw ADC
32-bit
64-bit
32:32
32:64
64:64
64:128
Event data format / Timer
Single event rate
Coincidence event rate

## Slide 24
Start
Read 8 bytes of data
Check the two MSB of the 8 bytes of data
Find pattern “00”, …, “01”?
An event format status word (00000)?
Yes
Yes
Determine the event data format
No
End
No
Algorithm to decode list mode data file

## Slide 25: Status Words
Provide ancillary information
Format
  64 bits marked by “00” beginning each byte
  Last byte begins “01”
  Format flag indicates type of word
  Payload contains data
64-bit status word

## Slide 26: Event Words
Raw ADC
  32 bits
Single event
  32 or 64 bits
Coincidence event
  32, 64, or 128 bits
Format
  Most-significant bit always “1”
Ex. 32-bit single event word

## Slide 27
Data In
Status word
Event word
Single Event
Coincidence event
Raw ADC
32-bit
64-bit
32:32
32:64
64:64
64:128
Event data format / Timer
Single event rate
Coincidence event rate

## Slide 28: Status Word – Event data format / Timer
Bit 63-62, 55-55, 47-46, 39-38, 31-30, 23-22, 15-14: “00”
Bits 7-6: “01”
Bit 61-57: status word type – format/timer word = “00000”
Bit 56: single or coincidence
Bits 53-48: event word type (i.e. raw ADC)
Bits 45-44: system config (i.e. small config)
Bits 43-40: status word frequency (i.e. every 1 ms)
Remaining 30 bits: timer
Event data format / Timer word

## Slide 29: Status Word – Coincidence event rate
Bit 63-62, 55-55, 47-46, 39-38, 31-30, 23-22, 15-14: “00”
Bits 7-6: “01”
Bit 61-57: status word type – coincidence rate word = “00001”
Bit 56,53,52: status word frequency (i.e. every 1 sec)
Bits 51-48: coincidence event rate status word counter
Remaining 36 bits: coincidence event counter
Coincidence event rate word

## Slide 30: Status Word – Single event rate
Bit 63-62, 55-55, 47-46, 39-38, 31-30, 23-22, 15-14: “00”
Bits 7-6: “01”
Bit 61-57: status word type – single event rate word = “00010”
Bit 56,53,52: status word frequency (i.e. every 1 sec)
Bits 51-48: single event rate status word counter
Remaining 36 bits: single event counter
Single event rate word

## Slide 31
Data In
Status word
Event word
Single Event
Coincidence event
Raw ADC
32-bit
64-bit
32:32
32:64
64:64
64:128
Event data format / Timer
Single event rate
Coincidence event rate

## Slide 32: Single Event - Raw ADC
Bit 31: “1”
Bits 30-17: address
Bit 16: unused
Bits 15-10: 64-level counter to create ADC train
Bits 9-0: raw ADC data
64 raw ADC data points form 1 single event curve
32-bit raw ADC data

## Slide 33: Single Event – 32-bit data
Bit 31: “1”
Bits 30-11: address
Bits 10-0: payload data
  Time mode, energy mode, test mode, flood map mode, user-defined mode
32-bit single event data

## Slide 34: Single Event – 64-bit data (not recommended)
Bit 63: “1”
Bit 32: “0”
Bit 31: “1”
Bit 0: “1”
Bits 62-43: address
Bits 42-33,30-1: payload data
64-bit single event data

## Slide 35
Data In
Status word
Event word
Single Event
Coincidence event
Raw ADC
32-bit
64-bit
32:32
32:64
64:64
64:128
Event data format / Timer
Single event rate
Coincidence event rate

## Slide 36: Coincidence event – 32-bit  64-bit
Two 32-bit single event words
Bit 31: set to 1 if valid coincidence data; 0 if not
3264-bit coincidence event data

## Slide 37: Coincidence event – 32-bit  32-bit
Bit 31: “1”
Bit 30: set to 1 if valid coincidence data; 0 if not
Bits 29-0: determined by user (i.e. coincidence pair ID and time differential)
3232-bit coincidence event data

## Slide 38: Coincidence event – 64-bit  128-bit
Two 64-bit single event words
Bit 63: set to 1 if valid coincidence data; 0 if not
64-bit single event data

## Slide 39: Coincidence event – 64-bit  64-bit
Bit 63: “1”
Bit 62: set to 1 if valid coincidence data; 0 if not
Bits 61-0: determined by user (i.e. coincidence pair ID and time differential)

## Slide 40
Data In
Status word
Event word
Single Event
Coincidence event
Raw ADC
32-bit
64-bit
32:32
32:64
64:64
64:128
Event data format / Timer
Single event rate
Coincidence event rate

## Slide 42: Graphical User Interface (GUI) design
Top level design

## Slide 43: Graphical User Interface (GUI) design
Analog gain settings
CFD settings
Energy window settings
Serial communication
Energy data analysis
TDC calibration
Data acquisition
Data analysis SW package
(currently in Matlab)
Crystal decoding
Delay compensation
Time analysis
Sinogram analysis
System configuration database management
Flood map display
(for block detector)
SSPM event display
Chinh Vu and Michael Malus also contributed to the GUI design

## Slide 44: Graphical User Interface (GUI) design
System characterization